## Slide 1
DRILLPRINT
Shazam for drilling failures — deterministic, explainable, physics-grounded, real-time.
It recognizes drilling dysfunctions from rig sensor data the way Shazam recognizes a song in a noisy bar.
Johnpaul Okeke · August 2026 · 6 of 8 build phases delivered · 119/119 tests passing

## Slide 2
What it watches for
Three drilling failures destroy bits and drillpipe. Each one leaves a distinct spectral signature in the rig's sensors — a fingerprint.
▮
STICK-SLIP
The drillstring winds up like a torsion spring, then the bit whips free — over and over. Seen in surface torque.
▮
BIT WHIRL
The bottom assembly rolls around the borehole wall backwards, hammering it. Seen in lateral vibration.
▮
BIT BOUNCE
The bit lifts off and slams the hole bottom in rhythm. Seen in axial vibration and weight-on-bit.
No machine learning. Every alert decomposes into an auditable chain — detection is proof, not probability.

## Slide 3
How it works
1
LISTEN
Stream rig sensors — torque, RPM, vibration
2
FINGERPRINT
Reduce the signal to its strongest spectral peaks, hashed in pairs
3
NORMALIZE
Re-sample per revolution — fingerprints survive speed changes
4
MATCH
Look up against a physics-generated library of failure episodes
5
PROVE
Two independent statistics must both defeat a chance model
ALERTS
AMBER
advisory in seconds
RED
confirmed, with statistical proof attached

## Slide 4
What was built
M0
Signal engine — spectrograms, fingerprints, matcher
● DONE
M1
Physics simulators for all four drilling conditions
● DONE
M2
Per-revolution matching (the research contribution)
● DONE
M3
Fingerprint library — 176 episodes, versioned & approved
● DONE
M4
Live streaming service with two-tier alerts + digital twin feed
● DONE
M5
Benchmark vs. a conventional baseline
○ MACHINERY DONE · full run in progress
M6
Control-room UI + cinematic 3D rig view
● LIVE & PLAYABLE
M7
One-command demo mode & scenario player
○ NOT STARTED
Spec-first build: a 40-finding verification study hardened the design before code; 8 further spec errors were caught and fixed by the implementation itself.

## Slide 5
Verified numbers
2 ms
to match one window against the full library (target: 10 ms)
22 s
to build the entire 456,000-print library (budget: 5 min)
0
false alarms on the pump-noise trap designed to fool it
8.5 s
to confirm whirl during a live speed ramp — the hard case
119
automated tests, all passing
10⁻¹³⁸
chance that a confirmed whirl match was luck

## Slide 6
Was it a success?
YES
The core science works and is proven by tests: fingerprints survive speed changes, detections carry mathematical proof, and the pump-noise decoy never fools it. It runs end-to-end today: live sensors in, amber-to-red alerts out, with a playable 3D rig that animates every failure from real data. Left to finish: the full benchmark report, the one-command demo (M7), and UI polish.
drillprint · engine + library + streaming service + rig view · built spec-first with every design decision auditable